## Slide 1: BLB 2.0

## Slide 5: Choices to make:
Parts re-use
Size
Cooling
Doors
Window positioning

## Slide 6: Parts re-use
There are many parts that can be re-used between the two scanners:
  Aluminium profiles (x8) (Limits housing size) €120-150 out of €240-310
  Hinges (x9) €80-100 out of €100-130
  Angle brackets (x24) €160-210 out of €220-290
  Screws/bolts (Many) Too annoying to calculate
  Switches (x6) €30-40 out of €50-70
  Latches (x5) €40-50 out of €50-70
  Lights
Do we want to re-use these parts and be unable to use the scanner during building?
Panels cant be re-used and are about €4850-6300 (though we might be able to source some from the workshop €2000ish)

## Slide 7: Size
Current size:
  980x500x660
New Size:
  1680x740x900 (Maximizing parts re-use)
  Tables size: 2000x750
    Need to be able to open the doors comfortably
    Do we want to have extra working space on the table? Fit a control computer?
    Position FORS spectrometer inside or outside?

## Slide 8: Cooling
Active Cooling
  Just fans running through the gap
Passive cooling
  Complicates design significantly
Cooling of the scan head as well?
Openings on multiple sides?
Cool air in
Cool air in
Hot air out

## Slide 9: Doors
Horizontal swing doors
  Would require 4 doors with safety systems and limit access size to two doors

## Slide 10: Doors
Vertical swing doors
  Dangerous if they fall, and very heavy piece
  Upwards swinging: extra safety for radiation (since its normally closed) but extra danger of falling on person whilst working in the machine
  Downwards swinging: safer for the user, but can still swing down and hit them

## Slide 11: Doors
Slide doors
  Slightly complicated design and limit access size to two doors, but slightly larger than swing doors
Probably can’t have windows

## Slide 12: Window positioning
Should we put in the lead glass window?
If so, where?
  One of the doors
    Adds complexity and weight to the door

## Slide 13: Window positioning
  The rear panel
    View of the scanner may be blocked by the object if scanning vertically
    Directly in the beam path if scanning vertically